## Slide 1: Comparing Risks Across Building Water Use Types with QMRA
Ryan Julien*, Jade Mitchell,
Md. Rasheduzzaman, Wanyu Huang, Yolanda Brooks,
Patrick Gurian, & Mark Weir
Notes: And that brings me to the next topic, comparing risks across building water use using QMRA.
This work is based on a multi-institution collaboration stemming from the QMRA Interdisciplinary Instructional Institute.

## Slide 2: Outline
Introduction
Model
Results
Conclusions
Image: QMRA Wiki (qmrawiki.canr.msu.edu/)
Notes: During this talk, I’ll give a brief introduction to the problem formulation, explain the model structure used to evaluate risks, discuss results and explain some general conclusions.
For those of you who are unfamiliar, the QMRA framework is shown here, and consists of
hazard identification
formulating a dose-response relationship for the hazard
Determining the dose using an exposure assessment
Characterizing risks; and finally
To risk management where steps

## Slide 3: Introduction
Goal: Assess differences in pathogen health risk across common water use types
Pathogens
  Mycobacterium Avium complex (MAC)
  Legionella spp.
Hospital/group home setting
  Pathogen concentrations from studies in these homes
  Higher-risk population
QMRA Framework
Water uses considered:
  Showering
    Conventional (13 LPM)
    Low-flow (7 LPM)
  Toilet Flushing
    Flushometer (FOM)
    Pressure-assisted (PAT)
    High-efficiency (HET)

## Slide 4: Model Form
DP – Exposure dose of each pathogen, P
R – Recovery efficiency
  0.84 (Hamilton, 2019)
CP – Concentration of pathogen P
  MAC - Triangular dist. (de Moulin 1988)
  Legionella - Lognormal dist. (Fillipis 2018)
RB – Breathing rate
  Normal dist. (USEPA, 2011)
t – Exposure duration
  Shower = 15 min
  Toilet = 30 min (reflects sampling methods)
Caer, d – Concentration of aerosolized droplets of diameter d (in microns)
Vd – Volume of each aerosol of diameter d
- Deposition efficiency for aerosols of diameter d
RP – Risk of infection for each pathogen, P
kP – Dose-Response parameter
  (Hamilton et al. 2017)
C – Exposure route conversion factor
  (Hamilton et al. 2017)

## Slide 6: Pathogen Input Concentrations
MAC
  Data: de Moulin et al. 1988
  Triangular distribution based on minimum, median, maximum
  Hot/cold water simulated separately
    Shower uses mixed, toilet uses cold
Legionella
  Data: Filipis et al. 2018
  Fit a log-normal distribution
    Raw data available
  Hot and cold water assumed to contain same concentration

## Slide 7: Common Correlations within Model
MAC in Low-Flow Shower
Breathing Rate
  Correlated with dose (0.80) and risk (0.62)
Concentration
  With dose (0.54) and risk (0.42)
Risk
  With dose (0.77) and k (0.63)

## Slide 8: Results – Showering
Low-flow showers exhibited slightly lower risk
  True for both MAC and Legionella
    Higher flowrate ⇒ more aerosols
  This analysis does not consider the effects of stagnation

## Slide 9: Results – Toilet Flushing
Risks for toilets
  FOM > PAT > HET
  True for both pathogens
  Differences more pronounced for MAC

## Slide 10: Conclusions
Risks across all water use are low
  Used dose-response factor for general population
Additional water use appears to increase risk
  Effect of stagnation not considered
Pathogen concentrations highly variable
Potential improvements
  Additional data for pathogen concentration estimates
  Consider water age/stagnation
  Incorporate dose-response for vulnerable populations

## Slide 11: Thank You & Questions